## Slide 1
• socket(): Creates a new socket.
• sockaddr_in: Structure containing an internet address.
• bind(): Binds the socket to an address and port number specified by the sockaddr structure.
• listen(): Marks the socket as a passive socket that will be used to accept incoming connection requests.
• accept(): Extracts the first connection request on the queue of pending connections and creates a new socket for that connection.
• ntohs(): Converts a short integer from network byte order to host byte order.
• ntohl(): Converts a long integer from network byte order to host byte order.
• read()/recv(): Reads data from a socket.
• write()/send(): Writes data to a socket.
• connect(): Establishes a connection to a specified socket.

## Slide 2
struct sockaddr {
u_short sa_family;
char sa_data[14];
};
• sa_family: This field specifies the address family, which tells the system what kind of address is being used. For internet addresses, this will usually be set to AF_INET.
• sa_data: This is a placeholder for the actual address data. It can hold a variety of address information depending on the address family. For internet addresses, it will contain the port number and IP address.

## Slide 3
AF_INET is a constant defined in the socket programming interface that stands for “Address Family: Internet”. It is used to specify that the address family in use is for IPv4 addresses. In other words, when you are creating a socket or specifying an address structure, AF_INET indicates that the addresses will be in the IPv4 format.
Here are some key points about AF_INET:
• IPv4 Address Family: AF_INET indicates that the socket is using the IPv4 protocol for addressing. IPv4 addresses are 32-bit addresses typically represented in dot-decimal notation (e.g., 192.168.1.1).
Usage in Socket Programming:
• When creating a socket with the socket() function, you specify AF_INET to indicate that you want to create a socket that communicates over the IPv4 protocol.
• When setting up the address structures, you set the sin_family field to AF_INET to indicate that the structure is being used for IPv4 addressing.

## Slide 4
struct sockaddr_in {
u_short sin_family;
u_short sin_port;
struct in_addr sin_addr;
char sin_zero[8];
};
• sin_family: This field is similar to sa_family and specifies the address family. For internet addresses, this will be AF_INET.
• sin_port: This field holds the port number. The port number is used to identify specific processes or network services.
• sin_addr: This field is a structure of type in_addr that holds the IP address.
• sin_zero: This is a padding field used to make the structure the same size as struct sockaddr. It’s not used for anything specific and should be set to zero.

## Slide 5
struct in_addr {
u_long s_addr;
};
• s_addr: This field holds the IP address in a 32-bit format (IPv4 address).

## Slide 6: Summary
These structures are used to handle socket addresses in network programming:
1. struct sockaddr: A generic address structure used for various types of addresses.
2. struct sockaddr_in: A more specific structure used for IPv4 internet addresses, including the IP address and port number.
3. struct in_addr: A structure used specifically to store an IPv4 address.
When programming with sockets, you’ll typically use sockaddr_in for internet addresses and cast it to sockaddr when calling functions that require a generic socket address. The sin_family field will indicate that the address is an internet address (IPv4), and the sin_port and sin_addr fields will specify the port and IP address, respectively.

## Slide 7: Header File: in.h
1. Address Family and Protocol Families
#define AF_INET 2 // Address family for IPv4
#define PF_INET AF_INET // Protocol family for IPv4
2. Structures
• struct in_addr: Represents an IPv4 address.
• struct sockaddr_in: Represents a socket address that includes an IPv4 address and port number.

## Slide 8
struct in_addr {
uint32_t s_addr; // 32-bit IPv4 address
};
struct sockaddr_in {
sa_family_t sin_family; // Address family (AF_INET)
in_port_t sin_port; // Port number (16 bits, network byte order)
struct in_addr sin_addr; // IPv4 address
unsigned char sin_zero[8]; // Padding to make the structure the same size as struct sockaddr
};
2. Structures
• struct in_addr: Represents an IPv4 address.
• struct sockaddr_in: Represents a socket address that includes an IPv4 address and port number.

## Slide 9
3. Macros for Special Addresses
#define INADDR_ANY ((uint32_t)0x00000000) // Any incoming address
#define INADDR_LOOPBACK ((uint32_t)0x7f000001) // Loopback address (127.0.0.1)
#define INADDR_BROADCAST ((uint32_t)0xffffffff) // Broadcast address
#define INADDR_NONE ((uint32_t)0xffffffff) // Error value

## Slide 10
4. Byte Order Conversion Functions
uint32_t htonl(uint32_t hostlong); // Host to network long
uint16_t htons(uint16_t hostshort); // Host to network short
uint32_t ntohl(uint32_t netlong); // Network to host long
uint16_t ntohs(uint16_t netshort); // Network to host short

## Slide 11
5. Prototypes for Internet Address Manipulation
• inet_pton: Converts an IP address in text form to binary form.
• inet_ntop: Converts an IP address in binary form to text form.
int inet_pton(int af, const char *src, void *dst);
const char *inet_ntop(int af, const void *src, char *dst, socklen_t size);